Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 200 0:00 0 0:40 * 210 0:30 2 2:40 N 230 0:30 7 7:40 N 250 0:30 11 11:40 O 270 0:30 15 15:40 O 300 0:30 19 19:40 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 360 0:30 23 23:40 480 0:30 41 41:40 720 0:30 69 69:40 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Umbilical flush is to be formally logged 40 FEET NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 100 0:00 0 0:50 * 110 0:40 3 3:50 L 120 0:40 5 5:50 M 140 0:40 10 10:50 M 160 0:40 21 21:50 N 180 0:40 29 29:50 O 200 0:40 35 35:50 O 220 0:40 40 40:50 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 240 0:40 47 47:50 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Umbilical flush is to be formally logged 50 FEET NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 60 0:00 0 1:00 * 70 0:50 2 3:00 K 80 0:50 7 8:00 L 100 0:50 14 15:00 M 120 0:50 26 27:00 N 140 0:50 39 40:00 O 160 0:50 48 49:00 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 180 0:50 56 57:00 200 0:40 1 69 71:00 240 0:40 2 79 82:00 360 0:40 20 119 140:00 480 0:40 44 148 193:00 720 0:40 78 187 266:00 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 60 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 50 0:00 0 1:10 * 60 1:00 8 9:10 K 70 1:00 14 15:10 L 80 1:00 18 19:10 M 90 1:00 23 24:10 N 100 1:00 33 34:10 N 110 0:50 2 41 44:10 O 120 0:50 4 47 52:10 O 130 0:50 6 52 59:10 O 140 0:50 8 56 65:10 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 150 0:50 9 61 71:10 160 0:50 13 72 86:10 170 0:50 19 79 99:10 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 70 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 40 0:00 0 1:20 * 50 1:10 10 11:20 K 60 1:10 17 18:20 L 70 1:00 23 24:20 M 80 1:00 2 31 34:20 N 90 1:00 7 39 47:20 N 100 1:00 11 46 58:20 O 110 1:00 13 53 67:20 O 120 1:00 17 56 74:20 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 130 1:00 19 63 83:20 140 1:00 26 69 96:20 150 1:00 32 77 110:20 180 0:50 35 85 121:20 240 0:50 5 52 120 179:20 360 0:50 29 90 160 280:20 480 0:50 59 107 187 354:20 720 0:40 17 108 142 187 455:20 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 80 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 30 0:00 0 1:30 I 40 1:20 7 8:30 J 50 1:20 18 19:30 K 60 1:20 25 26:30 L 70 1:10 7 30 38:30 M 80 1:10 13 40 54:30 N 90 1:10 18 48 67:30 N 100 1:10 21 54 76:30 O SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 110 1:10 24 61 86:30 Z 120 1:10 32 68 101:30 130 1:10 5 36 74 116:30 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 90 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 25 0:00 0 1:40 * 30 1:30 3 4:60 I 40 1:30 15 16:40 K 50 1:20 2 24 27:40 L 60 1:20 9 28 38:40 N 70 1:20 17 39 57:40 O 80 1:20 23 48 72:00 O 90 1:10 3 23 57 84:40 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 100 1:10 7 23 66 97:40 110 1:10 10 34 72 117:40 120 1:10 12 41 78 132:40 180 1:00 1 29 53 118 202:40 240 1:00 14 42 84 142 283:40 360 0:50 2 42 73 111 187 416:40 480 0:50 21 61 91 142 187 503:40 720 0:50 55 106 122 142 187 613:40 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 100 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 20 0:00 0 1:50 * 25 1:40 3 4:50 H 30 1:30 7 8:50 J 40 1:30 2 21 24:50 L 50 1:30 8 26 35:50 M 60 1:30 18 36 55:50 N 70 1:20 1 23 48 73:50 O 80 1:20 7 23 57 88:50 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 90 1:20 12 30 64 107:50 100 1:20 15 37 72 125:50 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 110 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 15 0:00 0 2:00 * 20 1:50 2 4:00 H 25 1:50 6 8:00 I 30 1:50 14 16:00 J 40 1:40 5 25 32:00 L 50 1:40 15 31 48:00 N 60 1:30 2 22 45 71:00 O 70 1:30 9 23 55 89:00 O 80 1:30 15 27 63 107:00 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 90 1:30 19 37 74 132:00 100 1:30 23 45 80 150:00 120 1:20 10 19 47 98 176:00 180 1:10 5 27 37 76 137 284:00 240 1:10 23 35 60 97 179 396:00 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 120 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 10 0:00 0 2:10 * 15 2:00 1 3:10 F 20 2:00 4 6:10 H 25 2:00 10 12:10 J 30 1:50 3 18 23:19 M 40 1:50 10 25 37:10 N 50 1:40 3 21 37 63:10 O 60 1:40 9 23 52 86:10 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 70 1:40 16 24 61 103:10 80 1:30 3 19 35 72 131:10 90 1:30 8 19 45 80 154:10 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 130 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 10 0:00 0 2:20 * 15 2:10 2 4:20 G 20 2:10 6 8:20 I 25 2:00 2 14 18:20 J 30 2:00 5 21 28:20 K 40 1:50 2 16 26 46:20 N 50 1:50 6 24 44 76:20 O 60 1:50 16 23 56 97:20 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 70 1:40 4 19 32 68 125:20 80 1:40 10 23 41 79 155:20 90 1:30 2 14 18 42 88 166:20 120 1:30 12 14 36 56 120 240:20 180 1:20 10 26 32 54 94 168 386:20 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 140 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 0:00 0 2:30 C 10 2:20 1 3:30 E 15 2:20 3 5:30 G 20 2:10 2 7 11:30 H 25 2:10 4 17 23:30 K 30 2:10 8 24 34:30 L 40 2:00 5 19 33 59:30 N 50 2:00 12 23 51 88:30 O 60 1:50 3 19 26 62 112:30 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 70 1:50 11 19 39 75 146:30 80 1:40 1 17 19 50 84 173:30 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 150 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 0:00 0 2:40 D 10 2:30 1 3:40 F 15 2:20 1 4 7:40 H 20 2:20 3 11 16:40 J 25 2:20 7 20 29:40 K 30 2:10 2 11 25 40:40 M 40 2:10 7 23 39 71:40 N 50 2:00 2 16 23 55 98:40 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 60 2:00 9 19 33 69 132:40 70 1:50 1 17 22 44 80 166:40 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 160 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 0:00 0 2:50 D 10 2:40 2 4:50 F 15 2:30 2 5 9:50 H 20 2:30 4 15 21:50 J 25 2:20 2 7 23 34:50 L 30 2:20 4 13 26 45:50 M 40 2:10 1 10 23 45 81:50 O 50 2:10 5 18 23 61 109:50 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 60 2:00 2 15 22 37 74 152:50 70 2:00 8 17 19 51 86 183:50 90 1:50 12 12 14 34 52 120 246:50 120 1:30 2 10 12 18 32 42 82 156 356:50 180 1:20 4 10 22 28 34 50 78 120 187 535:50 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 170 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 0:00 0 3:00 D 10 2:50 3 6:00 F 15 2:40 3 6 12:00 I 20 2:30 1 5 17 26:00 J 25 2:30 3 10 24 40:00 L 30 2:20 6 17 27 53:00 N 40 2:10 3 14 23 50 93:00 O 50 2 9 19 30 65 128:00 Z SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 60 2:10 5 16 19 44 81 168:00 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 180 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 0:00 0 3:10 D 10 2:50 1 3 7:10 G 15 2:50 6 7 14:10 I 20 2:40 2 6 20 31:10 K 25 2:40 5 11 25 44:10 M 30 2:30 1 8 19 32 63:10 N SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 40 2:30 8 14 23 55 103:10 50 2:20 4 13 22 33 72 147:10 60 2:20 10 17 19 50 84 183:10 DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 190 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 3:10 1 4:20 - 10 3:00 1 4 8:20 - 15 2:50 1 4 10 18:20 - 20 2:50 3 7 27 40:20 - 25 2:50 7 14 25 49:20 - 30 2:40 2 9 22 37 73:20 - SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 40 2:30 2 8 17 23 59 112:20 - 50 2:30 6 16 22 39 75 161:20 - 60 2:20 2 13 17 24 51 89 199:20 - 90 1:50 1 10 10 12 12 30 38 74 134 324:20 - 120 1:40 6 10 10 10 24 28 40 64 98 180 473:20 - DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 200 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 3:20 1 4:30 - 10 3:10 2 4 9:30 - 15 3:00 1 5 13 22:30 - 20 3:00 4 10 23 40:30 - 25 2:50 2 7 17 27 56:30 - 30 2:50 4 9 24 41 81:30 - SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 40 2:40 4 9 19 26 63 124:30 - 50 2:30 1 9 17 19 45 80 174:30 - DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 210 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-10 STANDARD AIR WITH NITROX OR AIR DECOMPRESSION BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 100 90 80 70 60 50 40 30 20 10 5 3:30 2 5:40 - 10 3:20 2 5 10:40 - 15 3:10 2 5 16 26:40 - 20 3:00 1 3 11 24 42:40 - 25 3:00 3 8 19 33 66:40 - 30 2:50 1 7 10 23 47 91:40 - SUPERIOR OPERATIONAL DEPTH / TIME LIMITS 40 2:50 6 12 22 29 68 140:40 - 50 2:40 3 12 17 18 51 86 190:40 - DIVE PROCEDURES – TABLE 1-10 Modified in Water Decompression Tables with Nitrox or Air in Water Stops IN WATER PHASE * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours * Ascent procedures Previous bottom time must have been such that divers repet group was no greater than ‘O’ 60 feet per min to the indicated stop or surface if no stops Decompression time as specified begins on arrival at stop depth Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Do not include ascent time as part of stop times Refer to Table 1-12 for new RGD at the end of the surface interval Delays at earlier stops are not to be compensated for at later water stops Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) *50/50 Nitrox Switch LOSS OF NITROX Switch to 50/50 Nitrox at 100 feet during ascent If there is a loss of Nitrox, switch diver to Air and decompress according to table Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive 220 FEET Umbilical flush is to be formally logged NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.