Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 52 1:36 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 5:36 K 90 1:36 3 10 15 1 50:36 N 120 1:36 3 10 23 2 63:36 0 150 1:36 3 10 31 2 71:36 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 180 1:36 3 10 39 2 79:36 Z DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 70 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 40 2:00 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 6:00 * 70 2:00 3 10 14 1 50:00 M 85 2:00 3 10 20 2 61:00 N 100 2:00 3 10 26 2 67:00 O 115 2:00 3 10 31 2 72:00 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 130 2:00 3 10 37 2 78:00 150 2:00 3 10 44 3 90:00 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 80 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 32 2:24 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 6:24 J 60 2:24 3 10 14 1 50:24 M 70 2:24 3 10 20 2 61:24 N 80 2:24 3 10 25 2 66:24 N 90 2:24 3 10 30 2 71:24 O 100 2:24 3 10 34 2 75:24 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 110 2:24 3 10 39 2 80:24 120 2:24 3 10 43 3 89:24 130 2:24 3 10 48 3 94:24 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 90 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 26 2:48 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 6:48 I 50 2:48 3 10 14 1 50:48 L 60 2:48 3 10 20 2 61:48 N 70 2:48 3 10 26 2 67:48 O 80 2:48 3 10 32 2 73:48 O 90 2:48 3 10 38 2 79:48 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 100 2:48 3 10 44 3 90:48 110 2:48 3 10 49 3 95:48 120 2:24 2 4 10 53 3 103:24 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 100 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 22 3:12 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 7:12 H 40 3:12 3 10 12 1 49:12 L 50 3:12 3 10 19 1 56:12 M 60 3:12 3 10 26 2 68:12 N 70 3:12 3 10 33 2 75:12 O 80 2:48 2 3 10 40 3 89:48 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 90 2:48 2 4 10 46 3 96:48 100 2:48 2 5 10 51 3 102:48 110 2:48 2 12 10 54 3 112:48 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 110 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 18 3:36 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 7:36 H 30 3:36 3 10 9 1 46:36 J 40 3:36 3 10 16 1 53:36 L 50 3:36 3 10 24 2 66:36 N 60 3:12 2 3 10 32 2 77:12 O 70 3:12 2 4 10 39 2 85:12 O 80 3:12 2 5 10 46 3 98:12 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 90 3:12 4 8 10 51 3 108:12 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 120 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 4:00 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 8:00 F 30 4:00 3 10 12 1 50:00 M 40 4:00 3 10 21 2 64:00 N 50 3:36 2 3 10 29 2 74:36 O 60 3:36 2 5 10 37 2 84:36 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 70 3:36 2 7 10 45 3 99:36 80 3:36 6 10 10 51 3 112:36 90 3:36 10 14 10 56 3 125:36 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 130 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 13 4:24 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 8:24 G 25 4:24 3 10 11 1 49:24 J 30 4:24 3 10 15 1 53:24 K 35 4:24 3 10 20 2 63:24 N 40 4:00 2 3 10 24 2 70:00 N 45 4:00 2 4 10 29 2 76:00 O 50 4:00 2 6 10 33 2 82:00 O 55 4:00 2 7 10 38 2 88:00 Z 60 4:00 2 9 10 43 3 100:00 Z SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 65 4:00 4 11 10 48 3 109:00 70 3:36 2 7 13 10 51 3 119:36 DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 140 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 11 4:48 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 8:48 G 25 4:48 3 10 13 1 51:48 K 30 4:48 3 10 18 1 56:48 L 35 4:24 2 4 10 23 2 70:24 N 40 4:24 5 7 10 27 2 80:24 N 45 4:24 6 9 10 33 2 89:24 O 50 4:00 2 7 11 10 38 2 100:00 O 55 3:36 2 5 9 14 10 44 3 121:36 Z DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 150 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 9 5:12 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 9:12 F 20 5:12 3 10 11 1 50:12 J 25 5:12 3 10 16 1 55:12 K 30 4:48 2 4 10 21 2 68:48 M 35 4:48 4 7 10 26 2 78:48 N 40 4:24 3 6 9 10 32 2 92:24 N 45 4:00 3 4 8 12 10 38 2 108:00 Z DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 160 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26 SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 7 5:36 3 NOT TO EXCEED 5 MINUTES 10 MINUTES O2 ** 9:36 F 20 5:36 3 10 13 1 52:36 J 25 5:36 3 10 19 1 58:36 L 30 5:12 5 7 10 23 2 77:12 M 35 4:48 4 6 9 10 29 2 90:48 O 40 4:24 4 4 8 13 10 36 2 108:24 O DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 170 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26x SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 5:36 4 6 NOT TO EXCEED 5 MINUTES 10 20 1 10 MINUTES O2 ** 59:36 NO REPET DIVES 30 4:48 2 3 5 10 10 40 2 88:48 SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 45 4:00 2 4 6 12 18 10 50 2 120:00 NOTE: NO REPETITIVE DIVES ALLOWED ON THESE TABLES DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 180 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26x SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 5:36 2 4 6 NOT TO EXCEED 5 MINUTES 10 20 1 10 MINUTES O2 ** 61:36 NO REPET DIVES 30 5:12 3 5 8 12 10 50 2 103:12 SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 45 4:24 2 5 10 18 26 10 50 2 145:24 NOTE: NO REPETITIVE DIVES ALLOWED ON THESE TABLES DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 190 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26x SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 6:00 2 5 7 NOT TO EXCEED 5 MINUTES 10 20 1 10 MINUTES O2 ** 64:00 NO REPET DIVES 30 4:48 2 4 6 10 16 10 50 2 112:48 SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 45 4:45 2 5 12 20 30 10 70 3 167:48 NOTE: NO REPETITIVE DIVES ALLOWED ON THESE TABLES DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 200 feet * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26x SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 6:24 3 4 8 NOT TO EXCEED 5 MINUTES 10 20 1 10 MINUTES O2 ** 65:24 NO REPET DIVES 30 5:12 2 4 7 12 18 10 60 3 132:12 SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 45 5:12 2 6 14 24 36 10 70 3 181:12 NOTE: NO REPETITIVE DIVES ALLOWED ON THESE TABLES DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 210 FEET * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.

Table 1-26x SURFACE DECOMPRESSION USING OXYGEN WITH NITROX OR AIR IN WATER STOPS BOTTOM TIME (MINS) TIME TO 1ST STOP IN WATER Stops (mins) at Depths (feet) SURFACE INTERVAL * IN CHAMBER ON OXYGEN NO OF AIR BREAKS ASCENT DECOMP TIME (MINS) REPET GROUP Breathing Nitrox or Air 80 70 60 50 40 30 50 40 15 6:24 2 4 5 10 NOT TO EXCEED 5 MINUTES 10 20 1 10 MINUTES O2 ** 91:24 NO REPET DIVES 30 5:36 2 5 9 14 20 10 60 3 139:24 SUPERIOR DIVING OPERATIONAL DEPTH/TIME LIMIT 45 5:36 2 6 16 30 42 10 70 3 195:36 NOTE: NO REPETITIVE DIVES ALLOWED ON THESE TABLES DIVE PROCEDURES – TABLE 1-26 Surface Decompression Using Oxygen with Nitrox or Air in Water Stops IN WATER PHASE CHAMBER PHASE * Ascent procedures Diver is recompressed to 50 feet in 30 seconds and is to be breathing oxygen within 3 minutes of arriving at 50 feet 25 feet per minute to the first stop Ascent time between stops & from 30 feet to surface is ONE MINUTE Remain at 50 feet for 10 minutes then ascend to 40 feet in 1 minute Decompression time as specified begins on arrival at the stop depth On arrival at 40 feet the first air break is given prior to starting Oxygen time at this depth Do not include ascent time as part of stop times Breath Oxygen for the time listed broken into cycles of 20 minutes interspersed with 5 minute air breaks Delays at earlier stops are not to be compensated for at later stops *50/50 Nitrox Switch ASCENT FROM 40 FEET Switch to 50/50 Nitrox at 100 feet during ascent ** On completion of total Oxygen time at 40 feet surface the diver at the rate 4 feet per minute (10 minutes) Nitrox decompression mix is not to be connected to the manifold until the diver passes 100 feet On surface divers umbilical is to be flushed thoroughly with air prior to starting next dive Diver to breath Oxygen during the entire ascent. Umbilical flush is to be formally logged LOSS OF NITROX * REPETITIVE DIVES – Are only permitted after a minimum surface interval of 6 hours If there is a loss of Nitrox, switch diver to Air and decompress according to table Previous bottom time must have been such that divers repet group was no greater than ‘O’ Refer to table 1-10 for Repetitive Group Designator (RGD) not to exceed ‘O’ Refer to Table 1-12 for new RGD at the end of the surface interval Using new RGD refer to Table 1-13 for Residual Nitrogen Time (RNT) 220 Feet * Surface Interval Upon surfacing the diver has 3 and a half minutes maximum to start recompression in the chamber NOTE: On any occasion that the Depth or Bottom Time falls within 2 feet or 2 minutes of a Depth or Time increment of a schedule use the next Deeper and/or next longer schedule.